## Slide 2: Assignment #1 Due Date Jan 29th
Write a Matlab code test a 10 GS/s ADC 8-bit ADC. First, generate an input sequence of fin. Second, generate sampled sequence and their digitized versions. Take 8192 points FFT and from the FFT find SNR, SFDR, SINAD, and ENOB.
Add non-linearity and spec the maximum non-linearity the front-end can tolerate without losing more than 1.5-bit ENOB. Identify the nonlinear tones in the FFT
Add random noise and find the maximum random noise the front-end can without losing more than 1-bit ENOB
Add the effect of jitter in the code and comment on how jitter impacts the performance.
Submission must include FFT plots, results and observation. Please also send the source code. This is an individual project.